## Slide 1: Article propose

## Slide 2: novel online approach of multi-modal relational graph network to dynamically integrate visual and kinematics information through interactive message propagation in the latent feature space.

## Slide 3: PERIOR WORKS

## Slide 4
NN based Kinematic data:
  hidden Markov models
  linear classifiers with hand-crafted metrics
  long short-term memory (LSTM)
  multi-task recurrent neural network
  multi-scale recurrent network (offline)
NN based Visual data:
  deep convolutional neural networks
  Temporal convolutional network (TCN)
  recurrent convolutional network
  3D convolutional network
  Symmetric dilated convolution
NN based Kinematic and visual data
  Joint prediction of motion and surgical state in robot assisted surgery

## Slide 5: Experiments

## Slide 6: Experiment 1
Train and Test dataset : JIGSAWS (suturing and knot-typing)

## Slide 7: Experiment 2
In-house dVRK datasets from two centers: CUHK , JHU
Peg transfer task, a standard exercise in laparoscopic surgical training
Gesture:

## Slide 8: MODEL

## Slide 10: Visual Information Extraction Module
An RGB image ​ (current video frame) is fed into a Convolutional Neural Network (CNN) backbone - ResNet-18.
​ transformed into a spatial feature vector.
The spatial feature vectors are collected into a sequence.
When sample video end, The collected sequence is then processed by a Temporal Convolution Module , output vector .
TCN:
  Encoder {64,96,128}
  Decoder {96,64,64}

## Slide 11: Kinematic Information Extraction Module
TCP and LSTM received The entire sequence of kinematic data that corresponds to all the sampled video frames
TCP:
  temporal convolution layers are applied to this sequence to capture local patterns and dependencies efficiently
  The TCN pathway outputs a sequence of kinematic features
LSTM:
  Long-short term memory are applied to this sequence to capture long term temporal dependencies
  It outputs a feature vectors ,

## Slide 12: Graph convolution network - KV FUSION
Nodes:
  Left kinematics
  Right kinematics
  Video

## Slide 13: Define adjacency matrix A
“Vision to motion”
“Motion to vision”
“Hands interaction”

## Slide 14
Aggregation function:

## Slide 15: GCN layer output

## Slide 16: Classification prediction

## Slide 17: Loss function

## Slide 18: Experiments Results

## Slide 19: Experiment 1

## Slide 21: Experiment 2